## Slide 1: Loss Minimization Control of an Induction Motor Drive
By
Aditya Kumar
(Roll no. 24M1355)
M.Tech (1st year)
Subject – EN 659
Under the guidance of
Prof. V.S.S. Pavan Kumar Hari
Department of Energy Science and Engineering
Indian Institute of Technology Bombay, Powai, 400076
May 2025

## Slide 2
Problem Statement
Conventional V/f drives do not ensure optimal efficiency, especially at light loads.
Efficiency drops with nonlinear torque-speed loads like fans or pumps.
Existing methods need accurate motor parameters, which vary with temperature and are hard to measure.
A parameter-independent control is needed to reduce losses while maintaining torque and speed.
Introduction
Types of inverter fed adjustable-speed IM drives
Open loop
Closed-loop
Cost effective but may not operate at max ɳ
Increased ɳ but require accurate model parameter knowledge

## Slide 3
Max efficiency only occurs when the intersection is at the speed corresponding to the inflection point of the efficiency-speed curve Nɳ,max
Operation at max efficiency frequently takes place at near rated load torque, at other operating conditions – reduced ɳ
Temp. variation – As temp of rotor increases, R2 increases, slope of T-ω reduces, operating point shifts such that ɳ reduces.
The Closed Loop – speed feedback advantage, control of inverter freq. ‘f’ to keep a constant ‘fr’ acc. to below eqn.
f = fr + Nm
Chosen rotor freq. – at rated speed, voltage and freq. If this rated rotor freq. results in operation near to max efficiency point, then this closed-loop, constant rotor freq. (CRF) inverter can offer a small efficiency improvement over the open-loop constant V/f control.
But max efficiency operation = fn. (eqv. circuit parameters, motor speed)
Max efficiency slip – more sensitive to rotor resistance than any other parameter (which itself varies with load profile, dynamic measurement – quite difficult, if at all possible)
Literature Review

## Slide 4
Kirschen et al. offered a testing and implementation of perturbing controller to minimize loss for a field-oriented controlled IM. [3]
Mehanna presents an adaptive controller modification of CRF inverter to operate at optimal efficiency. (Similar to [3], except that the extra complexity of field-oriented control is not required) [4]
Since the adaptive controller can be realized by modification of a constant V/f inverter, this paper implemented and tested this concept.
Advantage of Perturbing rotor frequency (PRF) : No need of motor parameters knowledge. So, variation in parameters due to temperature and saturation has no consequences.
Literature Review

## Slide 5: Theoretical Investigation
Modified Steinmetz equations (to account for freq. effects) :
R1 = R10 + c1f R2 = R20 +c2(sf)α Rms = cmfβ
where- R10 and R20 are the dc values of R1 and R2 , Constants c1, c2, α, β are determined from eqv. circuit evaluated at two frequencies
Let R2m + j X2m = (Rms + j Xms) II (R2 / s + j X2)
and ∆ = (Rms + R2 / s)2 + (X2 + Xms)2
P1 = 3V12R1 / [(R1 + R2m)2 + (X1 + X2m)2]
Pc = 3[(R2/s)2 + X22]V12Rms / ∆ [(R1 + R2m)2 + (X1 + X2m)2]
Pg = 3(Rms2 +Xms2)V12 (R2/s) / ∆ [(R1 + R2m)2 + (X1 + X2m)2]
PR = kNωm2
A) Efficiency Determination
where- P1 = Primary copper losses Pc = Core losses Pg = Air gap power PR = Rotation power losses
ωm = (1 - s) ωs =
For p =4
PR = kN[ π (1 - s) f]2

## Slide 6
For 4 pole, s = (πf - ωm ) / πf
ɳ = f6 (f, ωm)
∂ɳ / ∂f = 0  f = fɳ max (for a particular ωm)  Max efficiency operation
Limited range search approach is used.
(f is varied by small increments until
f = fɳ max is determined)

## Slide 7
Results of theoretical study –
Fig 3 : significant efficiency improvement for speed < 65% by PRF control over constant V/f control
Fig 4 and 5 : Lower voltage and increase frequency  Lower core losses  Lower total losses
B) Theoretical Predictions

## Slide 8: Experimental Investigation
2 modes of operation – (i) constant rotor frequency control, (ii) perturbing control
If ω’m > Ωm : DC link voltage reduces If ω’m < Ωm : DC link voltage increases
Perturbing subcontroller senses P and change δωr
If P reduces, another increment in previous direction If P increases, alter the direction
Inverter output freq. is adjusted until minimum input power is achieved.
An 8-b microprocessor-based implementation of the controller is used.
A) Controller Realization
Speed is regulated

## Slide 9
Two power conditioner-motor arrangements :
  Standard-efficiency motor with constant V/f control
  Standard-efficiency motor with perturbing rotor freq. control
Converter losses PcL and motor losses PmL : Measured by ‘Air calorimetric loss determination technique’
Test conducted : At 25, 50, 75 and 100% of rated speed
At each speed, shaft load torque of 1/4, 2/4, 3/4, 4/4 of 30 ft.lb (under steady state condition)
One additional point : 75% speed with 9/16 of 30 ft.lb
B) Test Descriptions

## Slide 10: Results of Tests
Comparison of overall system efficiency for V/f and PRF control –
Fig 10 : For 1/4 torque
Fig 11 : For 4/4 torque
Fig 12 : PRF control is best suited for nonlinear torque type load
Experimental observations –
Using V/f control :
ɳ1 = 78.6 % (at 75 % speed, 9/16 of rated torque)
and ɳ2 = 65.27 % (at 50 % speed, 1/4 of rated torque)
Using PRF control :
ɳ1 = 78.6 + 1.4 = 80 %
and ɳ2 = 65.27 + 7.46 = 72.73 %

## Slide 11: Conclusion
Small efficiency improvement  For near rated loads at low speeds
Significant efficiency improvement  For reduced loads at all speeds
Greatest efficiency improvement for loss minimization control with non-linear torque-speed loads.

## Slide 12: References
P. Famouri and J. J. Cathey, "Loss minimization control of an induction motor drive," in IEEE Transactions on Industry Applications, vol. 27, no. 1, pp. 32-37, Jan.-Feb. 1991.
A. Kusko and D. Galler, “Control means for minimization of losses in ac and dc motor drives,” IEEE Trans. Industry Applications, vol. IA-19, no. 4, pp. 561-570, July-Aug. 1983.
D. S. Kirschen, D. W. Novotny, and T. A. Lipo, “Optimal efficiency control of an induction motor drive,” IEEE Trans. Electron. Comput., vol. EC-2, no. 1, pp. 70-76, Mar. 1987.
C. Y. Mehanna, “Perturbing controller for minimum loss operation of induction machines,” M.S. thesis, Univ. Kentucky, Aug.1985.

## Slide 13
Thank You